## Slide 1
SmartFeed™
Chemical Conditioning System For Geotube® Dewatering Applications

## Slide 2: SmartFeed™ system General Description:
Smartfeed™ design solves chemical conditioning applications problems for various geotextile containment applications
Technology was designed to be compatible with dredging and diver operations, variability of flow and solids mass in the slurry
Technology is comprised of chemical makedown equipment, chemical-to-slurry mixing technology and on-board computer mass-balance reporting
Technology samples the slurry parameters every 15 seconds and recalculates the chemical dosage rate based on changes

## Slide 3: Polymer Make Down
SmartFeed™ system
does the following:
Meters neat emulsion or solution polymers
Mechanically mixes the product to begin proper activation
Upgradable to ratio the neat product to the incoming water flow
Transfers the solution to the application tank

## Slide 4: Polymer Make Up Skids
Designed to prepare and store solutions of emulsion grade polymer for onward dosing at the point of application.
Neat emulsion is metered through a progressive cavity pump and injected into the water flow, prior to passing through an inversion pump to ensure complete dissolution.
The resultant solution is transferred to a storage tank, ready for dosing at the point of application.

## Slide 5: Polymer Addition (non-post dilution)
Flocculation is the destabilization of a hydro-phobic colloidal suspension by bonding between colloidal particles using long polymer chains of high molecular weight (greater than 1 million).
The amount of polymer required to support continuous flocculation is dependent on the mass of dry solids entering the systems
The various portable unit are capable of handling up to 600 gpm @ .5% dilution concentration
This normally supports dredging projects in the 2000-3000 gallon per minute range

## Slide 6: Polymer Addition (post-dilution)
To reduce the need for fresh water when polymer demand is higher than 600 gpm @ .5% dilution
Units can be provided with post-dilution systems that allows filtrate from dewatering and or marine water for dilution of polymer in ranges up to 1,200 gpm for a .5% dilution polymer range. This supports dredging projects in the 2,000 – 4,000 gallons per minute range.

## Slide 7
Setup Page
SmartFeed™ system is a patent-pending technology for chemical dose management
Specific project operational parameters -- flow, solids range, lbs of polymer per dry ton of solids – are specified on this page

## Slide 8
Operational Page
The operational page allows operator to view, in real time, percent of dry solids, density, flow rate, pH and line pressure
The operational page selects which tubes are receiving flow

## Slide 9
Logging Page
Tube logging is updated at the end of each operational day.
This will download which tubes in the project received how many gallons and dry ton solids that day

## Slide 10
SmartFeed™
is a patent-pending technology of Mineral Processing Services LLC
James E. Meagher Mineral Processing Services LLC
PMB 128, 50 Market St. | South Portland, ME 04106
Telephone (207) 741-2955 | Fax (207) 799-3782
Web: http://www.smartfeedsystem.com | E-mail: jmmps@maine.rr.com